## Slide 1
For Physicists & Engineers using your
PianoRepair &Tuning
Laptop, Microphone, and Hammer
Bruce Vogelaar, Hans Robinson, Tatsu Takeuchi Virginia Tech
at
3:00 - 4:30 pm Hahn Hall North Rm 130
April 20, 2019
by
24 tone fun
Janko Keyboard
Fluid piano

## Slide 2
A pure sound pitch is a pressure wave travelling in air at speed with frequency , and wavelength .
note: any given gas molecule just goes back and forth.

## Slide 3
A piano string is fixed at its two ends, and can vibrate in several harmonic modes.
[v = speed of wave on string]
String instruments vibrate at specific frequencies:

## Slide 4
Converting string motion into sound is difficult:
    sound board
    resonant cavity
    electric pickups to amp to speaker

## Slide 5
time domain
frequency spectrum
Destructive Constructive
Add sounds together:
ok harsh

## Slide 6
frequency content determines ‘timbre’
Add sounds together:
Invert: given the ‘sum’,
what were the components?
Fast Fourier Analysis as in FFTuner @
www.phys.vt.edu/~vogelaar
please read the Help file which covers everything here in more detail
https://www1.phys.vt.edu/~kimballton/home/pub/piano/tuner-app/FFTuning.htm

## Slide 7
You might want a powered base microphone for the low frequencies.
C2 struck with key; log scale makes everything easier to see

## Slide 8
Why some notes sound ‘harmonious’ together
or rather, which notes don’t sound terrible together…. their harmonics are either matched or well separated
(In practice, you can hardly ever avoid harmonics of a fundamental.)
pure with harmonics
pure with harmonics
A
E
A
E+
frequency
harmonic
frequency
harmonic

## Slide 9
5th (3/2)
4th (4/3)
3rd (5/4)
Origins of the Just Temperament
Octaves are universally pleasing; to the Western ear, the 5th is next most important.
Octave (2/1)
frequency note 2
frequency note 1

## Slide 10
Going up by 5ths
12 times brings you very
near the same note
(but 7 octaves up)
this suggests 12 notes per octave
Equal temper: space by
‘cents’ between two notes: 1200 * log2(f2/f1)
Octave = 1200 cents
(“Wolf “ fifth is off by 23 cents.)
f
log2(f)
log2(f) shifted down into same octave
“Wolf ” fifth
Up by 5ths: (3/2)n
“Circle of 5th s”

## Slide 11
nearest just fraction:

## Slide 12
A guitar string is fixed at its two ends, and can vibrate in several harmonic modes.
[v = speed of wave on string]
Guitar

## Slide 13: Guitar
Spacing between frets:
Pressing a string between frets raises the tension in the string leading to the idea of harmonic tuning:
Play harmonics by lightly touching strings when strumming at 1/2, 1/3, 1/4 length, etc.

## Slide 14
Drums
(0,1)
(1,2)
radial and azimuthal nodes

## Slide 15: Drums
Modes of an ideal drumhead in a vacuum.
This is NOT what you’ll see on a real drum.

## Slide 16: Drums
First three are (0,1), (1,1), and (2,1).
Can confirm this by dampening out other modes (like playing harmonics on a guitar)

## Slide 17
5th (3/2)
4th (4/3)
3rd (5/4)
for equal temperament:
  tune so that desired harmonics are at the same frequency;
  then, set them the required amount off by counting ‘beats’.
Octave (2/1)
Back to pianos: what an ‘aural’ piano tuner does…

## Slide 18
I was hopeless,
and even wrote a
synthesizer to try
and train myself…
but I still couldn’t ‘hear’ it…
Perfect Fifth: from C, set G above it such that an octave and a fifth above the C you hear a 0.89 Hz ‘beating’
These beat frequencies are for the central octave.

## Slide 19
Perfect Fifth: the 2 cent beat frequency is easy to hear, when isolated.

## Slide 20: Is it hopeless? not with a little help from math and a laptop… we (non-musicians) can use a spectrum analyzer…

## Slide 21
True Equal Temperament Frequencies |  |  |  |  |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
C |  | 32.70 | 65.41 | 130.81 | 261.63 | 523.25 | 1046.50 | 2093.00 | 4186.01
C# |  | 34.65 | 69.30 | 138.59 | 277.18 | 554.37 | 1108.73 | 2217.46 | 
D |  | 36.71 | 73.42 | 146.83 | 293.66 | 587.33 | 1174.66 | 2349.32 | 
D# |  | 38.89 | 77.78 | 155.56 | 311.13 | 622.25 | 1244.51 | 2489.02 | 
E |  | 41.20 | 82.41 | 164.81 | 329.63 | 659.26 | 1318.51 | 2637.02 | 
F |  | 43.65 | 87.31 | 174.61 | 349.23 | 698.46 | 1396.91 | 2793.83 | 
F# |  | 46.25 | 92.50 | 185.00 | 369.99 | 739.99 | 1479.98 | 2959.96 | 
G |  | 49.00 | 98.00 | 196.00 | 392.00 | 783.99 | 1567.98 | 3135.96 | 
G# |  | 51.91 | 103.83 | 207.65 | 415.30 | 830.61 | 1661.22 | 3322.44 | 
A | 27.50 | 55.00 | 110.00 | 220.00 | 440.00 | 880.00 | 1760.00 | 3520.00 | 
A# | 29.14 | 58.27 | 116.54 | 233.08 | 466.16 | 932.33 | 1864.66 | 3729.31 | 
B | 30.87 | 61.74 | 123.47 | 246.94 | 493.88 | 987.77 | 1975.53 | 3951.07 | 
With a (free) “Fourier” spectrum analyzer we can set the pitches exactly!

## Slide 22: But first – a critical note about ‘real’ strings (where ‘art’ can’t be avoided)
strings have ‘stiffness’
bass strings are wound to reduce this, but not all the way to their ends
treble strings are very short and ‘stiff’
thus harmonics are not true multiples of fundamentals
fn is increased by a factor of

## Slide 23: A4 (440) inharmonicity
true 8x440 piano
which should match A7?

## Slide 24
Tuning the ‘A’ keys: Ideal strings
All the harmonics
On a log scale
Only the nearby octaves

## Slide 25
sounds ‘sharp’
sounds ‘flat’
How many cents from perfect.
Need to “Stretch” the tuning. Can not match all harmonics, must compromise  ‘art’
With 0.001 inharmonicity

## Slide 26
the FFTuner approach
Pluck/strike one string at a time
Tune octaves 3, 4, and 5 to their exact frequencies (setting the ‘temper’ and eliminating ‘stretch’ for this region as a reasonable first estimate).
For octaves 0, 1, and 2, tune their 8th, 4th, and 2nd harmonics respectively to match the same note in octave 3.
For octaves 6 and 7, tune their fundamentals to match the 2nd and 4th harmonics respectively from octave 5.
FFTuner pre-populates these choices to expedite the process. See Help file for lots of explanation.

## Slide 27: tools of the trade…

## Slide 28
! but some keys don’t work !
pianos were designed to be repairable
- likely need to remove ‘action’
(if you break a string tuning it, you’ll need to remove the ‘action’ anyway)
(remember to number the keys before removing them and mark which keys hit which strings)
“Regulation” Fixing keys, and making mechanical adjustments so they work optimally, and ‘feel’ uniform.

## Slide 29
a pain on spinets

## Slide 31: “Voicing” the hammers
NOT for the novice (you can easily ruin a set of hammers)

## Slide 32
Let’s now do it for real…
pin turning
unisons (‘true’ or not?)
tune using FFTuner
put it back together

## Slide 33
US Annual Piano Sales
getting harder to find…